HackRF One Bandwidth, Sampling Rae
9/17/18

Sampling and Bandwidth
Shannon-Nyquist Sampling Theorem tells us that for a sampling rate of 20 Msps (mega samples per second), a maximum bandwidth of 10 MHz can be expected.
The Hackrf One performs complex sampling, both I and Q, making its bandwidth the same as the sampling rate.

https://github.com/mossmann/hackrf/wiki/HackRF-One

Supported Sample Rates: 2 Msps to 20 Msps (quadrature)