HackRF One Transmit & Receive Power
9/17/18

Reference: https://github.com/mossmann/hackrf/wiki/HackRF-One

Transmit Power

“HackRF One's absolute maximum TX power varies by operating frequency:
- 10 MHz to 2150 MHz: 5 dBm to 15 dBm, generally increasing as frequency decreases
- 2150 MHz to 2750 MHz: 13 dBm to 15 dBm
- 2750 MHz to 4000 MHz: 0 dBm to 5 dBm, increasing as frequency decreases
- 4000 MHz to 6000 MHz: -10 dBm to 0 dBm, generally increasing as frequency decreases
Through most of the frequency range up to 4 GHz, the maximum TX power is between 0 and 10 dBm. The frequency range with best performance is 2150 MHz to 2750 MHz.
Overall, the output power is enough to perform over-the-air experiments at close range or to drive an external amplifier. If you connect an external amplifier, you should also use an external bandpass filter for your operating frequency.”

Receive Power
The maximum RX power of HackRF One is -5 dBm. Exceeding -5 dBm can result in permanent damage!
In theory, HackRF One can safely accept up to 10 dBm with the front-end RX amplifier disabled. However, a simple software or user error could enable the amplifier, resulting in permanent damage. It is better to use an external attenuator than to risk damage.
Per Wikipedia, -5 dBm is 316 microWatts

Antenna Power Usage
software-controlled antenna port power (max 50 mA at 3.3 V)