Packet Communications Test Results
9/25/2018

python gnuradio program: socktest.py generated from flow graph socket_pdu_.grc

python client program: simple_client.py

Start server program first, then client program

1. Send three message strings from client program to gnuradio socket server program. The flow graph is shown in Figure 1. The Socket PDU block acts a the TCP server, Host: localhost, Port: 8000

Figure 1: socket_pdu_tx_test Flow Graph

The Socket PDU receives messages from any client that connects to ‘localhost’, port 8000. Figures 2 and 3 show the client and server output messages. The gnuradio socket_pdu correctly received all three messages.

Figure 2: simple_client output

Figure 3: gnuradio socket server output

2. Send the message string “abcd” from client program to gnuradio socket server program and display the byte values. Figures 4 and 5 show the client and server program output. The message was correctly received. 61 62 63 64 are the hexadecimal values for ‘a’, ‘b’, ‘c’, ‘d’

Figure 4: gnuradio socket server output

Figure 5: simple_client output

3. Add the AsyncCRC32 block. Four additional bytes are added after the message bytes, as shown in figure 8.

Figure 6: Flow graph

Figure 7: client output

abcd bytes: 61 62 63 64
crc bytes: 11 cd 82 ed

Figure 8: gnuradio server output

4. Add FEC Async Encoder

The repetition encoder is used for the forward error correction. It generates 3 bits for each bit.

Example: 61 is 0110 0001

The repetition encoder generates 000 111 111 000 000 000 000 111 which is 1f 80 07

Figure 9: Flow graph with repetition FEC

Figure 10: gnuradio server output

Figure 11: client output