Relationship between Data Rate and Bandwidth

Definitions

bandwidth – range of frequencies, measured in Hz

rate – number of transmitted bits per time unit, usually seconds. Measured in bit/second or symbols/time unit.

The rate is proportional to the system bandwidth. The Shannon Capacity provides the maximum number of bits transmitted for a given system bandwidth in the presence of noise.

The achievable rate is smaller than the Shannon Capacity. Communications specification standards give the exact relation between system bandwidth and achievable rate.

Formulas

The bandwidth is related to the pulse (or symbol) rate Rs <= 2B. A sinc pulse of appropriate width has bandwidth B/2.

The bit rate is related to the pulse rate: Rb = k Rp where k is the number of bits carried by a symbol. (e.g. 4 bits per 16-QAM symbol)

Problem – Design a physical system that
- Fits over the channel bandwidth
- Conveys bits at a high rate
- Does so reliably, with few bit errors at the receiver
- Does so at feasible complexity at both tranmitter and receiver

1. Data Rate = W bps, Bandwidth = 2W Hz is rule of thumb.
2. The greater the bandwidth, the higher the data rate.
2. Keeping data rate constant, greater bandwidth means better quality of the received signal
3. The higher the center frequency, the higher the potential bandwidth
4. Narrower bandwidth, greater distortion (errors)

Theoretical Upper Bound of Information Transmitted by a device per second?

https://dsp.stackexchange.com/questions/22337/what-is-the-theoretical-upperbound-of-information-that-could-be-transmitted-by-a/22338

Scenario: no noise and no distortion of signal being transmitted

Can transmit up to Rp = 2B pulses per second. B is the available bandwidth.

Ex: Bandwidth, B = 10 kHz, then you can transmit up 20,000 pulses in one second. Rp is called the Nyquist rate.

Bits can be transmitted using pulses. In a scheme where 1 bit is transmitted per pulse, the bit rate Rb = Rp.

Ex: You want to transmit the bit sequence 1001. Can do this by transmitting pulses with amplitudes +1, -1, -1, +1. (The pulse shape does not matter). In this case the bit rate equals the pulse rate: Rb = Rp.

You can transmit more than one bit per pulse. Suppose the pulses can have four amplitudes: +3, +1, -1, -3. Then the bit sequence 1001 can be transmitted with 2 pulses, then Rb = 2 Rp.

Scenario: Noise is present

The received signal now includes noise. Assume you are transmitting with power equal to S watts, and the noise over the bandwidth B has N watts. The bit rate cannot be larger than the Shannon channel capacity,

C = B log_2( 1+S/N )

Both S and N are considered to have the same flat power spectrum over the bandwidth B.

C: channel capacity, in bits per unit time
B: channel bandwidth, in Hz
S(f) is the signal power spectrum
N(f) is the noise power spectrum
f is frequency in Hz

A simple system will operate well below the channel capacity. If you have a simple system, and try to communicate at a significant fraction of the capacity, there will likely be errors. The receiver will mistake a bit 1 for a bit 0 or vice versa. Depending on the application, a certain amount of errors can be tolerated. Example: In voice communications, one error out of 1000 bits (a bit error rate, BER of 0.001) is acceptable. Other systems are intolerable to errors.

Complex systems may or may not achieve more of the channel capacity.

Channel Capacity Approximations

https://en.wikipedia.org/wiki/Shannon%E2%80%93Hartley_theorem

If S/N >> 1, then C approx 0.332 B SNR where SNR = 10 log_10 S/N

If S/N << 1, then C approx 1.44 B S/N