OOK – Recognizing Preamble and Payload Binary Data
8/28/18

Objectives
1. Human recognition of preamble and payload data
2. Extract binary symbols from multiple-sample pulses

Human recognition of Preamble Data

File name: rx_preamble.grc

RF data source: scan_00_c313M_s8M.iq

Location: https://github.com/willydlw/sdrgnuradio/tree/master/ook/

The flowgraph image is shown below. It is the same flowgraph as rx_clean_binary with the following changes:
- Set the File Source repeat to No so it only reads through the file once.
- The gui sinks shown in darker gray have been disabled.
- The gui sink Y axis is scaled to Y min: -0.1, Y max: 1.5.

Running the flowgraph generates the output shown below. As the program runs, the user must wait a few seconds while the entire file is processed. After all file data is read, the data shown below is the last data transmission.

The 16 evenly spaced pulses on the left are the preamble. Zooming in on that section produced the image below. It is observed that the pulse period is 0.50 ms. The pulse is high for 0.25 ms and low for 0.25 ms.

The preamble allows us to determine the start of a data transmission. It can be used to establish the timing of individual bits for the rest of the transmission.

The preamble is followed by the data, also known as the payload. The next example will attempt to extract the payload data.

Extract Binary Symbols from Multi-sample Pulses

File Name: rx_payload.grc

Location: https://github.com/willydlw/sdrgnuradio/tree/master/ook

This flowgraph is an extension of the previous rx_preamble.grc file.

The following variables were added

Name	Value	Units

symbol_period	0.25 ms	seconds/symbol

working_samp_period	1/work_samp_rate	seconds/sample
1/400kHz = 0.00025 ms

samples_per_symbol	symbol_period/working_samp_period	samples/symbol
0.25/0.00025 = 100

It was physically observed that the preamble symbol pulse period was 0.25 ms. Each pulse period represents a single binary symbol. To extract that binary value, we have to determine the number of samples per symbol. With a working sample period of 400 kHz, there are 100 samples per symbol. We only need to keep one of these samples.
A Keep 1 to N block was added to the flow graph. The value for N is the samples_per_symbol value 100. This block extracts a single value for each N (100) samples.

The Decimated Baseband plot in the image below shows the binary symbol value for each of the pulses in the Clean Baseband plot.

To better see which dots correspond to which pulse, run the flow graph and zoom in on a particular time period.

Next, a Correlate Access Block is added to the flowgraph. The preamble 10101010101010101010101010101010 is stored as the access code and the threshold is set to 0. The threshold value tells gnuradio how strictly it must match the access code. A 0 says that every bit of the preamble must match. Setting it to an integer greater than zero allows for that many bit mismatch errors.

When the preamble is detected, a value of 2 is added to the last symbol of the preamble. When the last symbol is a 0, it is changed to 2. Similarly, when the last value is a 1, it is changed to a 3.

The last value of this preamble is a 0 and then changed to a value of 2. The Decimated Baseband plot below illustrates this.

End of preamble 0 has been changed to a 2 above.

Finally, a File Sink block is added to the flowgraph to save the binary symbols. The binary symbol data is saved to a file named ook.bin.