Details of a Simple PSK Transmitter Receiver gnuradio flow graph

Objective

Use gnuradio software to build a simple PSK transmitter receiver flowgraph.

- Transmitter
  - Start with a vector data source as the digital baseband
  - Modulate the digital baseband
  - Upshift the modulated signal to the carrier frequency
- Receiver
  - Tune to the carrier frequency
  - Filter to isolate the desired signal
  - Demodulate to reproduce the orginal digital baseband

PSK Transmitter Flow Graph

Functional Flow – There are two sources: vector source and signal source. The vector source is a sequence of 1’s and 0’s, which are the digital signal values to be transmitted. The signal source is a cosine signal at the carrier frequency.

Source Block Flow

- Vector Source
  - Repeat – The vector source digit is repeated n times, where n is the Interpolation setting.
  - Phase Mod – performs phase shift modulation
- Signal Source
  - Throttle – simulation, don’t overwhelm computer resources

- Multiply phase modulated signal times the throttled signal source
- Frequency Xlating FIR Filter

FM Receiver Functionality

- Tuning control
- Volume control
- Listen to audio using computer’s sound card
- Ability to save audio data to a file
- View radio signal

Flow graph variables

Name	Description	Default Value

samp_rate	Determines the amount of data	8e6	(8 MHz)
captured with the SDR when there is
a hardware source for the transmitter.

Note: In this example, there is no hardware source for the transmitter. This is a simulation that uses a vector source to provide a known digital sequence. Setting the sample rate to a value that is valid for a hardware source requires less changes to the flow graph when the vector source is replaced with a hardware source. Also, it may make the simulation more realistic.

work_samp_rate	Working sample rate.	Used to save	400e3	(400 kHz)
computing power.

Working sample rate – To save computational power, the flowgraph should work at the lowest sample rate possible without impacting signal quality.

The initial sample rate must be high to capture a large range of frequencies. Once the raw RF data has been captured and tuned to the desired frequency, this high sample rate is not needed to work with the captured data.

freq	tuning frequency	315e6 (315 MHz)

Note: Default value is the same as the OOK keyfob example. Set it to the desired tuning frequency.

center_freq	SDR center frequency that provides	313e6
RF data to the flow graph

Note: Default value is the same as the OOK keyfob example. Set it to the desired center frequency.

sensitivity	determines phase modulation	math.pi/2 (BPSK)

filter_cutoff	low pass cutoff frequency	100e3

filter_transition	low pass filter transition bandwidth	1e3

Transmitter Flow graph Blocks

Vector Source Block

Settings:

Vector: (-1, 1,1,1,-1,1,-1,1,-1,1,-1,-1,-1,-1,-1,-1,-1,-1,-1)
Repeat: Yes

Signal Source Block

Settings:
Sample rate: samp_rate
Waveform: Cosine
Frequency: carrier_freq
Amplitude: 1e3
Offset: 0

Repeat Block

Connected to output of vector source block. Provides a method of generating a square wave pulse by repeating the vector source digit the same number of times as the interpolation value.

Settings:
Interpolation	800

Example: The interpolation rate is set at 800.

The sample rate is 8 MHz.

Sample period is 1/8 MHz = 0.125 microseconds

Repeating the input 800 times results in a pulse length of 100 microseconds. (0.125 microseconds * 800)

This gives us a nice square wave signal.

To slow down signal and make the waterfall plots
easier to read the space and mark, multiply the
interpolation rate 800 by 1000 or some other
constant value.

QT Gui Time Sink Block

To see the repeat block output signal, connect a QT GUI Time Sink.

Settings:
Name	Digital Input
Number of points	16384
Sample rate	samp_rate

Phase Mod Block

Settings:
Sensitivity	sensitivity	Determines the type of phase modulation.

Note: a sensitivity of pi/2 means the phase will deviate -pi/2 when a -1 is input and +pi/2 when a +1 is input.

QT GUI Waterfall Sink Block

To see the phase mod block output signal, connect a QT GUI WaterfallSink.

Settings:
Name	Phase Mod Output
FFT size	1024
Center freq	0
Bandwidth	samp_rate

Receiver Flow graph Blocks

Frequency Xlating FIR Filter block – performs both tuning steps of frequency translation (shifting) and filtering. The signal is tuned by shifting the target frequency to the center and then filtering out all other signals, except for the target.

Settings

Center frequency: property determines the frequency shift. Gnuradio assumes input data is centered around 0 Hz. This property provides the new center frequency. For example, setting the Center Frequency property to 100 Hz will shift the RF data to the left by 100 Hz.

The flow graph data is not centered at 0 Hz. It is centered at the frequency defined by the variable center_freq. The variable freq is the frequency to which we want to tune our radio. For example, if center_freq is 96 MHz and freq is 96.7 MHz, we want to tune to 96.7 MHz. We want to shift the data by 700 kHZ or 0.7e6 (96.7 MHZ – 96 MHz). In terms of our variables, the expression freq – center_freq provides the desired shifting.

Center frequency: freq – center_freq

Taps: firdes.low_pass(1, samp_rate, filter_cutoff, filter_transition)

This calls a function that generates the taps for a low pass FIR filter with a gain of 1, operating at samp_rate, with a cutoff frequency of filter_cutoff, and a transition width of filter_transition.

For a low pass filter, maximum attenuation occurs at filter_cutoff + transition_width. Example: filter_cutoff is 100 kHz. Filters at the center frequency due to positive and negative frequencies. Maximum attenuation at 100 kH + 1 kHz or 101 kHz and greater. Or -101 kHz and lesser.

Because there are both positive and negative frequencies, associated with the shifted frequencies, this filter will pass the center frequency + / - filter_cutoff.

Decimation: After the filter block, the flow graph will be running at the working sample rate, using the following formula to calculate the required signal decimation:

int(samp_rate/work_samp_rate)

Complex to Arg	Demodulates filtered signal

Add Const Block	Adds constant value. Constant set to 0.

Binary Slicer Block converts float to byte

Uchar to Float Block needed to convert byte back to float to display in time sink

QT GUI Time Sink

Settings:
Name	Receiver Output
Number of Points	4096
Sample rate	work_samp_rate