FM Radio

- Start with a radio frequency (RF) source of data
- Tune and filter to isolated the desired signal
- Demodulate to produce the original transmitted signal
- Resample to play audio

FM Receiver

Functionality

- Tuning control
- Volume control
- Listen to audio using computer’s sound card
- Ability to save audio data to a file
- View radio signal

Flow graph variables

Name	Description	Default Value

samp_rate	Determines the amount of data	8e6	(8 MHz)
captured with the SDR

freq	frequency	94.9e6 (94.9 MHz)

volume	5 (range of 0 – 11)

center_freq	SDR center frequency that provides	Choose default based on
RF data to the flow graph	stations in your area

channel_width	Controls the width of the channel	105e3 (150 kHz)
filter.

Note: A filter channel width of 150 kHz causes the filter to preserve everything within a 150 kHz band around the tuned frequency. The bandwidth consumed by an FM broadcast is 150 kHz. Because there are both positive and negative frequencies, associated with the shifted frequencies, this filter will pass the center frequency + / - 75 kHz.

transition_width	Transition band width of channel	10e3 (10 kHz)
filter.

work_samp_rate	Working sample rate.	Used to save	400e3	(400 kHz)
computing power.

Working sample rate – To save computational power, the flowgraph should work at the lowest sample rate possible without impacting signal quality.

The initial sample rate must be high to capture a large range of frequencies. Once the raw RF data has been captured and tuned to the desired frequency, this high sample rate is not needed to work with the captured data.

Flow graph Blocks

Audio Sink – connects to computer’s sound card

Settings:

sample rate – choose rate to match computer’s sound card. Try one of the settings from the drop down list. Higher audio sample rates typically correspond to higher quality audio. Try 48 kHz.

Wav File Sink	- save received signal in a file for later audio playback.

Settings:

File – file name and path. Example: fm_audio.wav
Sample rate – same as that used for the Audio Sink. Example: 48000

Note: Use the same sample rate as used for the Audio Sink block, since this file will be used for later audio playback.

File Source – useful for testing the flowgraph. Uses raw RF data stored in a file.

Set the file property to the input file location and name.
Set Repeat to Yes

QT GUI Sink Block – used to visual data.

Connect it to the RF source block.

Settings
        Name	RF Source
Center frequency:	center_freq
Show RF freq:	YES
 Bandwidth:	samp_rate

Note: setting the center frequency to the variable center_freq and enabling the show RF property causes the x-axis on frequency plots to be centered around the actual center frequency, instead of 0.

The signal is tuned by shifting the target frequency to the center and then filtering out all other signals, except for the target.

Frequency Xlating FIR Filter block – performs both tuning steps of frequency translation (shifting) and filtering.

Settings

Center frequency: property determines the frequency shift. Gnuradio assumes input data is centered around 0 Hz. This property provides the new center frequency. For example, setting the Center Frequency property to 100 Hz will shift the RF data to the left by 100 Hz.

The flow graph data is not centered at 0 Hz. It is centered at the frequency defined by the variable center_freq. The variable freq is the frequency to which we want to tune our radio. For example, if center_freq is 96 MHz and freq is 96.7 MHz, we want to tune to 96.7 MHz. We want to shift the data by 700 kHZ or 0.7e6 (96.7 MHZ – 96 MHz). In terms of our variables, the expression freq – center_freq provides the desired shifting.

Center frequency: freq – center_freq

Taps: firdes.low_pass(1, samp_rate, channel_width, transition_width)

This calls a function that generates the taps for a low pass filter with a gain of 1, operating at samp_rate, with a cutoff frequency of channel_width, and a transition width of transition_width.

For a low pass filter, maximum attenuation occurs at channel_width/2 + transition_width. Example: channel_width is 150 kHz. Filters at the center frequency due to positive and negative frequencies. Maximum attenuation at 105 kHz/2 + 10 kHz or 85 kHz and greater. Or -85 kHz and lesser.

Decimation: After the filter block, the flow graph will be running at the working sample rate, using the following formula to calculate the required signal decimation:

int(samp_rate/work_samp_rate)

WBFM Receive Block

Wideband frequency demodulation

Settings:
Quadrature	work_samp_rate
Audtio Decimation	1

Rational Resampler Block

Used to reduce the sample rate down to the Audio Sink’s sample rate. Performs decimation and then interpolation.

Settings
Decimation	int(work_samp_rate)
Interpolation	48000	(same as Audio sink sample rate, requires integer)

Multiply Const Block

Used for the volume control in this application. Multiples by a constant value.

Settings:
Constant	volume